## Slide 1
PH3039 — Data Acquisition Laboratory
Spatial and Temporal Variance of
Particulate Matter Across
Diverse Micro-Environments
Dust Density Distribution:
A Comparative Environmental Study
11
Locations
3
Environments
86+
Data Points
MINI PROJECT

## Slide 2
INTRODUCTION
Why Indoor Air Quality Matters
People spend the majority of their time indoors
Airborne PM (particulate matter) can significantly affect respiratory function
Prolonged exposure leads to long-term pulmonary issues
Ventilation and human activity heavily influence dust distribution
Sensor & Methodology Overview
Sensor:
SHARP GP2Y1010AU0F optical dust sensor
Principle:
Infrared light scattering — voltage output ∝ dust concentration
MCU:
Arduino Nano for data acquisition at 1-second intervals
Locations:
11 sites across indoor, outdoor & semi-outdoor environments

## Slide 3
METHODOLOGY
01
Sensor Calibration
Controlled smoke source (burning matchstick) in sealed jar
Analog voltage recorded as smoke accumulated & dissipated
Calibration curve established: voltage → dust density (mg/m³)
Zero-dust baseline (VOC) confirmed at ~0.63 V
02
Data Acquisition
11 locations at University of Colombo measured
Arduino Nano ADC sampled at 1-second intervals
Formula: ρ = k × (V − VOC) applied to each reading
Indoor, outdoor, and semi-outdoor environments covered
03
Data Processing
Median filter (kernel size = 5) applied to raw ADC values
Eliminates transient noise while preserving real events
Filtered data plotted as dust density vs. time per location
Statistical analysis performed on representative dataset
Transfer Function: ρ (mg/m³) = k × (V − VOC) where k = dust sensitivity, V = measured voltage, VOC = zero-dust baseline voltage

## Slide 4
MEASUREMENT LOCATIONS — University of Colombo
INDOOR
Computer Lab
Electronics & Circuit Lab
Advance Lab
IFS Lab
Machine Lab
Higher PM in afternoons due to activity & stagnant air
OUTDOOR
University Ground
Under Banyan Tree
Around Chemistry Benches
Higher PM in mornings; thermal convection clears air by afternoon
SEMI-OUTDOOR
Building Lobby
ILC Building Ground Floor
SSC Building Ground Floor
Highly variable; dominated by cross-ventilation & airflow

## Slide 5
SENSOR CALIBRATION & LINEARITY VALIDATION
ADC Decay During Matchstick Smoke Calibration
700
500
300
100
Peak: 757 ADC
(~3.70 V)
Baseline: 120–130
(~0.63 V)
Sample Index →
Raw ADC Value
Exponential Decay Confirmed
Smooth, monotonic decay from ADC 757 to baseline — no dead zones or non-linear jumps detected.
Linearity Validated
Output voltage strictly proportional to particle density across the full measurement range.
Baseline Established
Resting ADC of 120–130 converts to ~0.63 V, consistent with manufacturer's specified VOC range.

## Slide 6
TEMPORAL VARIATIONS IN DUST DENSITY
Key Finding: Indoor and outdoor environments show opposing trends between morning and afternoon
INDOOR
Morning
Afternoon
↑ Accumulates through day
Human activity re-suspends settled dust. Restricted ventilation traps particulates in the breathing zone.
OUTDOOR
Morning
Afternoon
↓ Clears through day
Morning inversion layer traps dust near ground. Solar heating generates convective currents that disperse PM upward.
SEMI-OUTDOOR
Morning
Afternoon
↕ Highly variable
Dependent on immediate airflow patterns, cross-ventilation, wind direction, and adjacent outdoor PM levels.

## Slide 7
STATISTICAL ANALYSIS — University Ground (Early Afternoon)
86
Samples (N)
0.0396
Mean μ (mg/m³)
0.0063
Std Dev σ (mg/m³)
+1.28
Skewness
Descriptive Statistics
Metric
Value
Unit
Median
0.0383
mg/m³
Mode
0.0375
mg/m³
Minimum
0.0292
mg/m³
Maximum
0.0566
mg/m³
Range
0.0274
mg/m³
IQR
0.0058
mg/m³
Variance σ²
0.00004
(mg/m³)²
Statistical Insights
Tight central tendency: Mean, Median & Mode tightly clustered → confirms stable baseline dust level.
Minimal variance (σ = 0.0063): Median filtering successfully eliminated electrical noise from raw ADC signal.
Narrow IQR (0.0058 mg/m³): 50% of data points fall in a very tight band — sensor is consistently reliable.
Right skewness (+1.28): Models real physics — a hard lower floor with occasional transient spikes from wind or activity.

## Slide 8
DISCUSSION
Indoor Environments
Without natural thermal convection, human mechanical activity acts as a relentless engine for dust resuspension. Stagnant air traps particulates in the breathing zone. Active, engineered ventilation systems are essential for safe indoor air quality in educational spaces.
Outdoor Environments
Atmospheric thermodynamics act as a natural air purifier. The transition from morning inversion layers — which trap dust near the ground — to afternoon convective dispersion demonstrates how temperature gradients dictate local airflow and particulate density.
Instrumentation
The SHARP GP2Y1010AU0F sensor proved exceptionally reliable when coupled with digital median filtering. Positive skewness confirms the sensor accurately captured transient dust events against a stable clean-air floor, validating the entire experimental methodology.

## Slide 9
CONCLUSION
Key Takeaways from the Study
University of Colombo
PH3039 Data Acquisition Lab
Successfully built a low-cost, real-time PM monitoring system using Arduino Nano + SHARP GP2Y1010AU0F
Indoor spaces accumulate PM through the day due to human activity and poor ventilation
Outdoor environments self-clean in the afternoon via temperature-driven convective dispersion
Statistical analysis (σ = 0.0063, skewness = +1.28) confirms scientific validity of all measurements
Cost-effective framework — eliminates need for expensive commercial PM reference equipment